## Slide 1
SuperSpeed USB 3.0 Technology Overview and Industry Update

## Slide 2: Agenda
Introduction
Physical Layer Overview
Transmitter Test Requirements and Pitfalls
Calibration Caution
Receiver Test Requirements and Pitfalls
Synchronizing the USB analysis traces
Questions

## Slide 3: Worldwide shipment of USB-enabled Devices
Notes: USB 3.0 has been around for awhile now, but as the graphs above show the growth forecast over the next few years for this standard is exponential.
USB install base is 10+ billion and growing at 3+ billion a year.

## Slide 4
Product Development
Initial Deployment
Broad Deployment
SuperSpeed USB Timeline
2011
Compliance Program/Industry Enabling Development
USB 3.0 Electrical Compliance Test Specification
0.9RC
Wksp:
HI
Jan
1.0 Test
Spec – Pending ECN updates
Wksp: OR
April
Wksp:
OR
Jul
Wksp:
TPE
Sept
#78
#79
#77
#76
2012
#80
#81
Wksp:
OR
Nov
Wksp:
HI
Feb 6-10
#82
#83
#84
#85
(TBD)
Oregon
April
(TBD)
Taipei
Sept
Test Lab
Qualification – Pending resolution of USB 3.0 Gold Tree
(TBD)
Oregon
Nov
(TBD)
Oregon
July
SSIC spec
Work started
Notes: SSIC = SuperSpeed USB Inter-Chip
SSIC aims to support physical layer data rates starting at 1.2 to 2.9 Gbits/s and eventually extending up to 5.8 Gbits/s. It also plans a low power mode for data rates between 10 Kbits/s and 600 Mbits/s.
This isn't a race between the Thunderbolt and SuperSpeed, as they are addressing different applications. SSIC is addressing low-power, chip-to-chip connections for high-speed data such as between next-generation connectivity devices (802.11ac), applications processors and modems.

## Slide 5: Device Classes
Notes: USB defines class codes used to identify a device’s functionality and to load a device driver based on that functionality.
This enables every device driver writer to support devices from different manufacturers, and there are just a few out there, that comply with a given class code.

## Slide 6: USB 3.0 Physical Topology
Notes: The baseline structural topology is the same as USB 2.0. A tiered star topology with a single host at tier 1 and hubs at lower tiers to provide bus connectivity to devices.
The connection model accommodates backwards and forward compatibility for connecting USB 3.0 or USB 2.0 devices into a USB 3.0 bus.
Similarly, USB 3.0 devices can be attached to a USB 2.0 bus. The mechanical and electrical backward/forwards compatibility.
To diagnose fallback issues you have to simultaneously capture USB 2.0 and 3.0 traffic

## Slide 7: USB 3.0 Cable
Notes: USB 3.0 cables have eight primary conductors: three twisted signal pairs for USB data paths and a power pair.
In addition to the twisted signal pair for USB 2.0 data path, two twisted signal pairs are used to provide the SuperSpeed data path, one for the transmit path and one for the receive path.

## Slide 8: What is New With USB 3.0?
High Speed
480Mb/s NRZ half duplex 1 bi-directional link 4 signals (D+, D-, VBUS, GND)
Super Speed
5Gb/s 8B/10B coded 2 uni-directional links 4 additional signals
USB 2.0
USB 3.0
Notes: The biggest issues many customers are having when testing 3.0 is that they forget to test backward compatibility to 2.0 until the very end of design, or right before they ship, and many issues. They may pass all 3.0 requirements, and still fail 2.0 backward compatibility.

## Slide 9: What is different for USB 3.0
USB 2.0 High-Speed
    480Mbps
    NRZI, Half Duplex
    4 signals
        Dp, Dm, VCC, GND
    Cable Lmax= 5meter
    IconfigLP/FP = 100mA/500mA
    Isuspend = 500uA
    No SSC
    TX SQ at Near End
    No Host RX testing
USB 3.0 SuperSpeed
      5 Gbps
      8B/10B PRBS, Full Simplex
      8 signals
        4 USB2 , 4 SS Signals
      Cable Lmax= 3 meters
      IconfigLP/FP = 150mA/900mA
      Isuspend = 2.5mA
      SSC
      TX at End of Channel (Far end)
      RX Jitter tolerance
RX
Half Duplex
TX
RX
TX
RX
Full Simplex
TX
RX
TX
Notes: This slide shows a comparison of USB2 vs 3.0 for most of the biggest differences.
Obviously the speed change is the biggest difference
USB2 is half duplex (since twisted pair, bi directional) and 3.0 will be 8b/10 full simplex.
The block diagrams as the bottom of the slide show this difference.
USB2 has 4 signals, usb3 includes those 4 plus 4 additional signals.
For USB3 cable length details are “spec detail” because they haven’t been publically discussed yet so you should only verbally mention that the requirements don’t list a specific length yet, only performance requirements
I config limits will change by increasing approximately 50% to 150mA for low power devices and 750mA for high power devices. Again, this detail is not something you should give in text in the slides as it may change.
SSC is not supported in USB2, SSC is required for USB3

## Slide 10: Transmitter test requirements
(TX Far End)
Notes: This is the actual requirements of the Tx testing, that many of you are probably familiar with.

## Slide 11: TX Compliance Pitfalls
Notes: SSC modulation
SSC deviation
High Rj :flicker Jitter)
Poor de-emphasis :Causes eye failure at end of channel

## Slide 12
Calibration takes time
Calibration accuracy is critical to repeatable measurements
Calibration is where most users spend a majority of their time getting ready to test
Calibration Cautions and Pitfalls

## Slide 13
Turn on loopback by sending LFPS and required training sequences
The receiver stress pattern is BDAT with SKPs inserted as described in the standard. The pattern checker receives the looped stress pattern BDAT and recognizes bit errors
After sufficient test time the error counter of the pattern checker is read
      Pattern Generator: J-BERT, ParBERT
…stress pattern…training sequences…LFPS
stress pattern…
.
Pattern Generator
1.
2.
Pattern Checker
3.
Error Counter
Receiver Test Procedure External Error Counter
Pattern Checker: USB Protocol Analyzer; Ellisys USB Explorer and NOW JBERTB SER
Notes: 13

## Slide 14: Typical SuperSpeed Link Turn-on Sequence

## Slide 15: RX Compliance Pitfalls
Loopback issues
  Dut needs custom sequence
  DUT drops out easily
Calibration issues
  Inconsistent
  Poor Sj/Rj mod
  Automation of Cal
SSC deviation
invalid de-emphasis
  Great impact on TJ
Jitter tolerance failures
  10MHz, 20MHz, 33MHz
Compliant SJ
Poor/wrong SJ
Compliant SSC Profile
Intentional SSC Stress
Non-deterministic noisy SSC
Compliant De-emphasis
Non-compliant Overshoot
Notes: Absence of commas in compliance pattern can be an issue
Use alternating sequence because commas must not account into measurement
According to standard invalid 10B codes substituted by K28.4
Analyzers based on bit compare count too many errors

## Slide 16: Synchronizing the USB analysis traces from Protocol to Electrical
Diagnostic requires synchronization of protocol events to a physical trace on an Oscilloscope
Uses a physical connection between the two pieces of equipment
  SMA cable going from the ‘trigger out’ on the Agilent USB analyzer to the ‘trigger in’ on the Agilent scope.
  The scope should be setup to trigger on an ‘high to low’ alternating signal.
Trig IN / Trig OUT for use with other Agilent equipment

## Slide 17: USB 3.0 Jammer
  Can be used to create a variety of errors in a real OS environment that cannot necessarily be created by a generator
  Standalone unit (does not require analyzer)
  Example error types, events, packet modification, etc.
    LGOOD_n / LCRD_a out of order
    Corrupted ordered sets, LMPs, etc.
    CRC-5/16/32 errors
    LBA out of range
    Link connect / disconnect
    Power up / down (bus powered devices only)
    Missing or corrupt frames
    BOT or UAS Sense IU / Response IU errors
    The jammer can inject errors, modify or delete packets, or even turn off Vbus and turn it back on again
Notes: There are come cases where an exerciser/generator is required; there are many more cases where a jammer is a better fit.

## Slide 18: Agilent’s USB 3.0 – Total Solution
Receiver Test
Transmitter Test
Interconnect Test
DSOX90000A Infiniium
real time scope
SW
HW
Fixture
DUT
N4903B J-BERT High-Perf Serial BERT
N5990A Automatic SW for USB compliance
E5071C Option TDR
ENA Network Analyzer
U7242A
Test Fixture
U7243A USB Compliance Test Software
U7242A USB 3.0 Test Fixture
N8805A USB3.0 Protocol decode & triggering SW
DSO91304A Infiniium
real time scope
or
Bit-USB- CBL-0001
from BitifEye
Tx
Rx
Tx
De-emph
N4916A or N4916B or N4903B-002
with
USB3ET from USB-IF
Tx
Rx
Cable
Signal Condi-tioning
Protocol Test
(link/transaction layers)
U4611A/B
USB 3\2\1.1 Analyzer
U4612A Jammer
Rx
Tx
Rx
Tx
Notes: Point out the different instruments and which you did or will do a demo of.

## Slide 19: Demonstration

## Slide 20: Backup

## Slide 21: Agilent Digital Test Roadmap
DVI  DP & HDMI
Display Port 1.1  1.2
HDMI 1.3  HDMI 1.4
USB 2.0  USB 3.0 (5Gb/s)
Faster DDR3
DDR3 moving to 2133MHz
DDR4 expected in 2010+
Covering all key technologies in the computing eco system
PCIe 2.0  PCIe 3.0 (8GT/s)
2.5GT/s
5.0GT/s
8GT/s
1993
2003
2007
2009+
PCIe Speed Trends
PCIe 3.0
PCIe 2.0
PCIe 1.x
PCI
133MT/s
SATA 3G  SATA 6G
1.5 Gbps
3 Gbps
6 Gbps
1986+
2000
2002
2009
SATA Trends
SATA 3.0
SATA 2.0
SATA 1.0
ATA/ATAPI
USB devices
smart
phone
flash memory
USB HDTV receiver
HD Video
Camera
 | USB Flash | SD-Movie | USB Flash | HD-Movie
 | 1 GB | 6 GB | 16 GB | 25 GB
USB 1.0 | 22 min | 2.2 hr | 5.9 hr | 9.3 hr
USB 2.0 | 33 sec | 3.3 min | 8.9 min | 13.9 min
USB 3.0 | 3.3 sec | 20 sec | 53.3 sec | 70 sec
Faster font-side buses
forwarded clocking
QPI at 9.6 Gb/s and higher
Notes: If we look inside a single computing device, it is driven by multiple technologies. A single computer utilizes memory, PCIe, SATA, USB, HDMI, and DP of which devices then fan out to additional technologies of DigRF, Ethernet, more memory, more USB, and MIPI! Virtually every part of your design, whether inside or outside the box, relies
on these new technologies.
And these technologies are constantly changing. The ones that we are going to be focused on today are PCIe, USB and SATA

## Slide 22: N5990A Test Automation Software
Automated instrument control for:
  Setup calibration
  Compliance test
  Characterization test
  Support for debugging
Operator guidance
Sophisticated test reports
Supports full product characterization including transmitter measurements
Notes: Controls multiple instruments simultaneously
Automated setup calibration
Automated compliance and characterization
Step by step operator guidance
Complete test report

## Slide 23: Same Setup Supports Multiple Standards
J-BERT, oscilloscope and test automation software also cover
  PCI Express 1.1, 2.0
  SATA 1.5, 3, and 6Gb/s
  DisplayPort 1.1
Note: Additional applications may require additional instruments and accessories
DisplayPort
SATA
PCIe
Notes: The N5990A Test Automation Software and the main test instruments cover a wide range of applications. This slide shows the applications which can be addred with J-BERT and N5990A.
23

## Slide 24: LTSSM

## Slide 25: Flow Control (LCRD_x)
x is called Rx Header Buffer Credit Index. x= (A, B, C, D).
Signifies that a single Rx Header Buffer Credit has been made available.
Sent by a port after receiving a header packet that meets the following criteria:
      LGOOD_n has been or will be sent.
      The header packet has been processed, and an Rx Header Buffer Credit is available.
LCRD_x is sent in the alphabetical order of A, B, C, D, and back to A without skipping. Missing LCRD_x will cause the link to transition to Recovery.

## Slide 26: Rx Header Buffer Credit Advertisement
The Rx Header Buffer Credit Advertisement refers to exchange of available Local Rx Header Buffer Credits information.
Rx Header Buffer Credits Advertisement is done every time the port enters into U0.
A port shall initiate the Rx Header Buffer Credit Advertisement after sending LGOOD_n during Header Sequence Number Advertisement.
If a port enters U0 from Polling or Hot Reset, its Local Rx Header Buffer Credit Count is 4.
If a port enters U0 from Recovery, its Local Rx Header Buffer Credit Count is the number of Header Buffer space available at the receiver.

## Slide 27: U4612A USB 3.0 Jammer
  Can be used to create a variety of errors in a real OS environment that cannot necessarily be created by a generator
  Standalone unit (does not require U4611A/B analyzer)
  Example error types, events, packet modification, etc.
    LGOOD_n / LCRD_a out of order
    Corrupted ordered sets, LMPs, etc.
    CRC-5/16/32 errors
    LBA out of range
    Link connect / disconnect
    Power up / down (bus powered devices only)
    Missing or corrupt frames
    BOT or UAS Sense IU / Response IU errors
Notes: There are come cases where an exerciser/generator is required; there are many more cases where a jammer is a better fit.

## Slide 28: LMP Subtypes
Set Link Function : Used to force a port to accept all LGO_U1 and LGO_U2 Link Commands.
U2 Inactivity Timeout : Used to define the timeout from U1 to U2.
Vendor Device Test : Used for vendor-specific device testing and shall not be used during normal operation of the link.
Port Capabilities : It describes each port's link capabilities and is sent by both link partners after the successful completion of training and link initialization. Main capabilities advertized are:
      Link Speed supported (Must be 5GT/s)
      Number of HP Buffer at Tx & Rx side (Must be equal to 4)
      Direction : Downstream Port /Upstream Port

## Slide 29: LMP Subtypes Continued …
Port Configuration : Sent by the Downstream Port after Link Initialization. It describes the link speed at which the upstream port shall operate.
Port Configuration Response : Sent by the upstream port in response to a Port Configuration LMP. It is used to indicate acceptance or rejection of the Port Configuration LMP.