## Slide 1: PCI Express 3.0 Protocol Tool Solutions
Analyzer and Exerciser Products
Agilent Technologies
Digital Debug Solutions
Don Schoenecker PCIe Product Manager
Don_schoenecker@agilent.com
719-590-2553 July 13, 2013

## Slide 2: Table of Contents
System Configuration . . . . . . 3
    Backplane . . . . . . 5
    Probe Connection . . . . . . 8
    Embedded Controller and Analyzer Blade . . . . 9
Analyzer . . . . . . . 11
    Module Setup . . . . . . 12
    Probe Setup . . . . . . 13
    Open and Create PTU Files . . . . . 14
    Triggering . . . . . . 17
    Filtering . . . . . . 19
    Decoders (including Traffic and LTSSM viewers) . . . . 20
Exerciser . . . . . . . 25
    Adaptive Equalization . . . . . . 28
    LTSSM Tester . . . . . . 30
    Protocol Test Card (PTC3) . . . . . 34
Probes . . . . . . . 36
PCIe3 Total Solution . . . . . . 40
PCIe3 Products and Part Numbers . . . . . 41
Page

## Slide 3: PCI Express 3.0 Customer Challenges & Needs
1. Probing at 8GT/s
Close eye spec, need mechanism to recover signal ?
2. Significant changes in Logic Sub-Layer
3. Lack of stimulus for testing
No devices or limited devices on the market
How to probe (view) the signal without breaking the link?
How to probe (view) the signal without changing the actual signal?
Significant changes in the Link Training Status State Machine (LTSSM), how to validate all the different branches
Scrambling only, (no 8b/10b)
New scrambling polynomial
New encoding mechanism 128/130 (sync header)
Encapsulation changes at the TLP layer
Notes: F

## Slide 4: Agilent Digital Test Console U4300A Series PCI Express® 3.0 Protocol Test
Agilent offers
the complete platform for PCI Express® 3.0 Protocol Solution; “integrated analysis and stimulus tools and direct probing“
to address key challenges of PCIe 3.0 design and development
Protocol Analyzer
Exerciser/Emulation
Probing

## Slide 5: Example Gen3 x16 Traces (Online Packet Viewer)
Packet Viewer
Name it as you like! Customizable columns
Tag ID info
Lane info
Header info
Details and Payload info
Floating Tip Message
Notes: The GUI for PCIe 3.0 will leverage the existing Gen2 viewer, with changes to support the new decodes required in Gen3

## Slide 6: 5 in 1! LTSSM Tester & Exerciser with Future Scalability
LTSSM Tester & Scalability to Meet Future Testing Needs
PTC (Protocol Test Card) 3
LTSSM Tester
Single hardware, with multiple applications
  LTSSM Tester (opt LT3)
  Exerciser – EP emulation (opt EX3)
  Exerciser – RC emulation (opt EX3)
  Exerciser – EP/RC Gen2 MR-IOV emulation (opt MR2)
  PTC 3 & Compliance Assured Tests (investigation for the future releases)
Same form-factor as existing exerciser
EP/RC Emulation Exerciser
investigation for the future releases
Notes: 6

## Slide 7: RC/EP Emulation – Gen 1~3 DLLP & TLP I/O generation
Memory Read 32b
Memory Write 32b
I/O Request
Config Request
Completion with data

## Slide 8: System Configuration Trace Capture Between Root Complex (RC) and DUT
The U4321A, Solid Slot Interposer (SSI) probe is installed between the RC and DUT. Protocol packets (or traffic) are passed between the RC and the DUT through the SSI probe
The 4 cables attached to the SSI probe connect to the front of the U4301A, Protocol Analyzer module (not shown)
  Each SSI cable supports up to 8 PCIe 3.0 links. Therefore 4 SSI cables provide 32 links or 16 links in each direction or x16 bidirectional lanes
Bidirectional means protocol packets are passed back and forth between the RC and the DUT simultaneously
Downstream packets travel from the RC to the DUT. Upstream packets travel from the DUT to the RC
SSI Probe
8 link SSI probe cable
PCIe x16 connector
(previously hidden by DUT)
DUT

## Slide 9: System Configuration Backplane - Motherboard Substitute
Features of the N5316A Backplane
  Allow testing of the end nodes without access to RC system
  Provides power and clock to the DUT (Test Fixture)
    Power, Reset + AUX power for DUT if required
    Clock generator with/without SSC (Spread Spectrum) selectable
    Input for external reference clock
  All link widths supported – x1, x2, x4, x8, and x16
  Connectors: Two (2) independent x16 PCIe connector pairs (Link 1&3) & one x16 PCIe connector with loop back (Link 2)

## Slide 10: System Configuration PCIe3 Root Complex (CPU) Emulation using U4305A + N5316A
Benefits of RC Emulation and Backplane over a System Motherboard
DUT
RC Emulator U4305A
Backplane N5316A
Arbitrary Selected PCIe System/Motherboard
AUX Power Output
Power
Reset
(same)
  Problem accessing a PCIe3 motherboard or CPU
  Full PCIe 3.0 Protocol control of the DUT
  DUT functional isolation from the Root Complex

## Slide 11: System Configuration RC Emulator to DUT via Backplane Connection
Using the Link3 x16 connector pair, the U4305A Exerciser configured as a RC emulator is linked up to the DUT
This configuration also happens to be the same for using the PCIe 3.0 Protocol Test Card which will be discussed later
To capture trace, the SSI probe can be placed into either one of the two Link3 connectors for the Analyzer U4301A to intercept and capture the packets
DUT
U4305A
RC Emulator
Link3 x16 Connector Pair
(2nd connector hidden)
Link2 Connector Loopback
Link1 x16 Connector Pair
(2nd connector not shown)
or

## Slide 12: System Configuration Probes – SSI, Flying Lead (solder down), & Midbus Probes
The SSI, Midbus, and Flying Lead probes all serve the same purpose; send upstream and downstream protocol traffic to the analyzer
Ideally, all probes should have a large enough input impedance to be ‘invisible’ to both end-nodes of the channel under capture
Any probe can be used in place of the other provided there exists a probe connection point
  SSI requires a PCIe slot connector
  Midbus requires a PCI-SIG spec’d footprint masked into the trace copper
  Flying Lead requires an end node Si pin or test point differential pair within the ZIF width apart
Flying Lead Zero Insertion Force (ZIF) Tip soldered to Lane0 of the upstream and downstream channel
Midbus Footprint
Flying Lead (solder down)
Lane0 Upstream
Lane0 Downstream
Unused links

## Slide 13: System Configuration Analyzer & Embedded Controller in AXIe 2 Slot Chassis
2 Slot AXIe Chassis
PCIe 3.0 Analyzer Module
AXIe Embedded Controller
Controller VGA Output
3 USB 3.0 ports
(Keyboard, Mouse, External drive)
4 Probe POD ports with 4 channels per port
2 GbE Ethernet ports
Analyzer Module Trigger In/Out
  Embedded Controller
  Software host for Analyzer and Exerciser
  PCIe 2.0 x4 backplane connection from analyzer to host (No PCIe or USB cable connection required)
  Remote access via Gigabit Ethernet port
  160 GB 3½ inch SSD
  Windows® 7 (32 and 64 bit)
16 Channels per Analyzer Module

## Slide 14: System Configuration Putting it all together …PCIe 3.0 Protocol Tools Top to Bottom
DUT Emulation
Protocol trace capture using solder down probe
Two Slot Chassis
Protocol Analyzer
Embedded Controller. Host for the PTC 3.0, DUT Emulation, and Analyzer Module software
Probe cable attachment to Analyzer
Root Complex Emulation

## Slide 15: Analyzer software Overview

## Slide 16: Analyzer Module Setup
Set Memory size (64K to 4GB)
Probe wiring diagram
Link and Module configuration
Probe selection
Clock source
Lane configuration
Custom Lane mapping with Analyzer soft switch

## Slide 17: Analyzer - Probe Setup Selection, Connection, Lane Mapping
Slot Interposer
Mid Bus Probe
Solder Down Tip
Gen2 Probe Reuse Using Gen3 Adaptor
Lane Mapping
Probe Selection Menu
Module Configuration
Link Width

## Slide 18: Analyzer Open Existing .ptu File

## Slide 19: Analyzer Create a Custom .ptu File
Name the custom .ptu file

## Slide 20: Analyzer Tuning Modes
The probe tuning algorithm will apply an Analog Tune then a Fine Tune across each lane indicated in the probe lane-width setup
  Analog Tune is an Agilent proprietary ‘eye scan’ sweep of whatever signal is on the channel
  Fine Tune applies a digital tune to the result generated by the Analog Tune
    The Fine Tune will attempt to converge the probe lane transceiver values to 10-12 BER (accuracy is system dependent)
    Standard Tune Mode limits the number of Fine Tune attempts to converge a lane to 100 tries
    Quick Tune Mode limits the number of Fine Tune attempts to converge a lane to 10 - good for demos
    Fine Tune Previous Result Mode will apply a Fine Tune ONLY to a previously created .ptu file named in the ‘Select PCIe Phy Tuning file (.ptu)’
Select a Tuning Mode then …
Selecting Fine Tune Previous Result mode will run a Fine Tune ONLY on the “BDM Demo.ptu” file listed here
… click here to Perform a Tune
Tune progress bar
Tune progress bar

## Slide 21: Analyzer Triggering
Triggering Capabilities
  4 states supported in trigger sequencer
  Trigger sequencer supports
    Pattern matchers
    Protocol errors and events
    Counters
    Timers
    External Triggers in/out
Click, Drag & Drop
Text search for trigger term
Trigger Event Condition Window
Trigger Else Condition Window
Trigger position relative to available memory

## Slide 22: Analyzer Advanced Triggering Mode
  Advanced Trigger :
    Can specify a trigger event sequence
  Packet events are dropped into event boxes and sequencer
  Events can be dropped within a sequence level, in between levels, or replace an entire level

## Slide 23: Analyzer Packet Filtering Options
Pull Down Selection

## Slide 24: Analyzer Decoder Viewers Post Process Overview of Trace
Trace View
Available Decoders
Set Decoder Data Range
Compute Button Builds Decoder Data from the Trace Captured
Step Through Navigation Window Packet(s) Occurrences

## Slide 25: Analyzer Decoder Overview Traffic Viewer
Data Range computed from Trace capture
Post Process View of a Trace Capture
Decoder packet grouping
Packets decoded within the selected Data Range
Downstream, Upstream & Total packet occurrence
Computes packet occurrence from the captured trace file within the selected data range
Highlight packet(s) to jump too in the trace view using the Navigation control buttons
Packet Navigation control buttons

## Slide 26: Analyzer Protocol Trace and Decoder Viewers
Packet Viewer
Tag ID info
Name it as you like! Customizable columns
Floating Tip Message
Header info
Lane info
Details info
Gen3
Trigger Point
Decode Overview Selections

## Slide 27: Transaction Decode
Pane | Description
Transaction decode pane | The left pane displays a list of transactions. New decoders automatically work as they become available. Initial release has NVMe with PCIe; Under development: AHCI
Transaction overview pane | The right pane displays the number of occurrences of these transactions
Transaction decode pane
Transaction overview pane

## Slide 28: NVMe Queue Interface for Command Processing
Command Processing
3. Controller fetches command
4. Controller processes command
Command Submission
1. Host writes command to submission queue
2. Host writes updated submission queue tail pointer to doorbell
Command Completion
5. Controller writes completion to completion queue
6. Controller generates MSI-X interrupt
7. Host processes completion
8. Host writes updated completion queue head pointer to doorbell
Controller
Submission Queue Tail Doorbell
Completion Queue Head Doorbell
Fetch Command
Process Command
Generate Interrupt
Queue Completion
Queue Command
Process Completion
1
2
3
4
5
6
7
8
Ring Doorbell New head
Ring Doorbell New tail
Host
Host Memory
Submission Queue
Completion Queue
Tail
Tail
Head
Head

## Slide 29: Visualize Transaction: Understanding NVMe
2
3
4
5
6
8
Ring Doorbell New Tail
Fetch Command
Process Command
Queue Completion
Generate Interrupt
Ring Doorbell New Head
PCIe messages
NVMe Data
NVMe Command execution

## Slide 30: Analyzer LTSSM Decoder (pg 1of2)
Select LTSSM Navigation by
State or Transitions
Trace Capture Window
Link speed by state
Bubble view
Upstream traffic
Downstream traffic

## Slide 31: PCIe LTSSM Analyzer

## Slide 32: Analyzer LTSSM Decoder (pg 2of2)
Navigate window, Trace capture, Ribbon view, and Bubble view are correlated
Jump from state to state, upstream or downstream using arrow keys

## Slide 33: Linked LTSSM Flow
Reference Flow Chart
Navigate State Transitions

## Slide 34: PCIe Performance Overview
Pane | Description
Categories pane | The leftmost pane displays a list of categories for which statistics will be generated and displayed.
Performance Statistics pane | The middle pane displays a list of performance parameters for the category that you select in the Categories pane. For each of these parameters, statistics are displayed based on the link directions (upstream as well as downstream).
Performance Charts pane | The rightmost pane displays a performance chart

## Slide 35: Analyzer Performance Overview
Chart Pan and Zoom Controls
On/Off Performance Window switch
Check for License & Compute Completed Transactions
Notes: There are On/Off buttons to enable/disable each of the post process panes.
After loading an .ala config file you have to compute transactions and statistics to produce this display. Select a range and then select the compute button, just like in the Traffic or LTSSM overviews.
The compute occurs in two phases. In the first phase a transaction list is constructed from the packets captured in the config file. The second phase computes the performance statistics using the transaction list computed in the first phase and is much quicker than the first phase.

## Slide 36: Analyzer Performance Overview
Statistic Type
Statistic Type Tables
Setting Chart Sample Rate
Setting Markers on Chart

## Slide 37: Exerciser (Packet Generator) One Hardware, Multiple Applications
End Node Emulation
  Root Complex & DUT
LTSSM Tester
  State specific solicitation
Protocol Test Card
  Specification compliance tool
IO Virtualization
  Multi Root and Single Root
EP/RC Emulation Exerciser
LTSSM Tester
PTC 3.0
MRIOV & SRIOV

## Slide 38: Exerciser Feature Capability High Lights
2.5, 5, & 8 GT/s speed support at x1, x4, x8, & x16 lane widths
Autonomous (Adaptive) Equalization capable for phases 2/3
DLLP and TLP I/O generation
ECRC checker
Packet level Error Insertion
5 Virtual Functions for PCIe, MRIOV, and SRIOV
PCIe 3.0 compliance measurement for DUT and BIOS (x1 only)
New

## Slide 39: Exerciser software Overview

## Slide 40: Exerciser General & Adaptive Equalization Setup
Pre, Post, & Data cursor ON – Exerciser will determine proper coefficient values
Transmitter pre-emphasis and auto Boost is ON – Exerciser will determine the correct tap and Boost settings

## Slide 41: Exerciser Pattern Matcher & Power Management Setup

## Slide 42: Exerciser LTSSM Tester GUI
Test result log file
52 total tests available
Run/Stop Test
High lighted test details
Prerequisite condition. The test will not move on without passing these prerequisites

## Slide 43: Exerciser End Node Emulation – DLLP & TLP Packet Generator
Memory Read 32b
Memory Write 32b
I/O Request
Config Request
Completion with data
Up to 5 Physical Functions for I/O Virtualization
Click, Drag & Drop Template into Function window
Left dbl click mouse anywhere on function to open packet editor

## Slide 44: Exerciser Config Space Setup
Config Space Setup for up to 5 Physical Functions of I/O Virtualization
Slide down to see all Config Space setup for PCI Express Capabilities
Notes: Here is a snap shot of what the LTSSM looks like. We will focus on the test case, changing speed from 2.5G (Gen1) to 8G (Gen3). We walked through the state machine in the last webinar, so you know the different transitions that need to take place for the speed change. And in the software, in the setup window this is also spelled out for you.
When you run this test, the LTSSM will step through the different stages of the state-machine, and force the dut to also make the same changes in its state-machine. By looking at the responses from the DUT, the exerciser will know if the DUT has taken the correct arcs in the state-machine and made the correct transitions or not.
!

## Slide 45: Exerciser Error Insertion
ACK/NAK Error Insertion
Dynamic Link Layer Error Insertion
Request and Completion Errors
Notes: Here is a snap shot of what the LTSSM looks like. We will focus on the test case, changing speed from 2.5G (Gen1) to 8G (Gen3). We walked through the state machine in the last webinar, so you know the different transitions that need to take place for the speed change. And in the software, in the setup window this is also spelled out for you.
When you run this test, the LTSSM will step through the different stages of the state-machine, and force the dut to also make the same changes in its state-machine. By looking at the responses from the DUT, the exerciser will know if the DUT has taken the correct arcs in the state-machine and made the correct transitions or not.
!

## Slide 46: Exerciser PTC Tester GUI
Gen2 and Gen3 Tests available
Run/Stop Test
Test Description
Select Message Framing to trigger Analyzer for trace capture
Gen2 and Gen3 Tests available
View & Print Log
Notes: Here is a snap shot of what the LTSSM looks like. We will focus on the test case, changing speed from 2.5G (Gen1) to 8G (Gen3). We walked through the state machine in the last webinar, so you know the different transitions that need to take place for the speed change. And in the software, in the setup window this is also spelled out for you.
When you run this test, the LTSSM will step through the different stages of the state-machine, and force the dut to also make the same changes in its state-machine. By looking at the responses from the DUT, the exerciser will know if the DUT has taken the correct arcs in the state-machine and made the correct transitions or not.
!

## Slide 47: Exerciser PTC Log File Sample
Notes: Here is a snap shot of what the LTSSM looks like. We will focus on the test case, changing speed from 2.5G (Gen1) to 8G (Gen3). We walked through the state machine in the last webinar, so you know the different transitions that need to take place for the speed change. And in the software, in the setup window this is also spelled out for you.
When you run this test, the LTSSM will step through the different stages of the state-machine, and force the dut to also make the same changes in its state-machine. By looking at the responses from the DUT, the exerciser will know if the DUT has taken the correct arcs in the state-machine and made the correct transitions or not.
!

## Slide 48: Explored PCIe Capabilities

## Slide 49: Enable Memory Space and Setup Bar0
Enable for Memory Space
Setup Bar0
Press Apply

## Slide 50: Program Controller Registers
Press Initialize Admin Queue
Setup Admin SQ
Setup Admin CQ

## Slide 51: Once Setup is Complete You Can…
  Create, Delete, and View Submission and Completion Queues
  Submit an NVMe command and view its completion status
  Reset the NVMe controller capabilities

## Slide 52: NVMe Conformance Testing

## Slide 53: Exerciser (Packet Generator) One Hardware, Multiple Applications
End Node Emulation
  Root Complex & DUT
LTSSM Tester
  State specific solicitation
Protocol Test Card
  Specification compliance tool
IO Virtualization
  Multi Root and Single Root
EP/RC Emulation Exerciser
LTSSM Tester
PTC 3.0
MRIOV & SRIOV
5. NVMe RC emulation

## Slide 54: NVMe Exerciser Features
Scan and initialize the NVMe capabilities of the DUT.
NVMe controller registers of DUT are available for viewing and editing.
Configure the Admin submission and completion queue attributes.
Set the interrupt mechanism to be used and then configure the selected interrupt mechanism.
Define, view, and edit the MSI-X table of the DUT.
Create multiple I/O submission and completion queues
Configure submission queue Head and Tail pointers and completion queue head pointer.
Add NVMe commands to submission queues and submit these to the NVMe DUT. The commands are available as predefined templates.
View the commands and their subsequent completions in the completion queues.
Create PRP lists and PRP entries that can be used in the submitted NVMe commands for data transfer.

## Slide 55: Gen3 Probes
Flying Lead
(Solder Down)
Interposer
Midbus
Gen2 to Gen3 Adaptor

## Slide 56: Probing ESP (Equalization Snoop Probe) Technology
  Super receiver to account for a wide spectrum of losses (probing at different points on the bus).
  Auto tuning, to account for being plugged into any location in the channel.
  Compensation for probe cable losses.
Unequalized Signal at 8GT/s
Equalized Signal at 8GT/s
Protocol Analyzer Probe with Custom Tunable Equalization (ESP)

## Slide 57: Probing
U4321A Slot Interposer :
  Slot Interposer available with first release
  All link widths (x1, x4, x8, x16)
U4322A Mid-bus probe :
  Footprints are available now
  KOV available now
  Full size mid-bus probe available (x8 bidirectional)
  Investigating ½ size mid-bus probe and flying lead set
U4324A Flying Lead (solder down):
  4 channels per probe
  Full customizable mapping per channel
  N5426A ZIF tip kit to connect probe to DUT
Notes: Talk about Gen3 being closed eye spec. At probe points, the signal from specs right now is going to be a closed eye. Need special techniques to ensure that the signal can be probed without breaking the bus, and also getting enough signal to the analyzer for debug.
Agilent has some unique capabilities in this area that we have used for other technologies (disk drive read channel technology within Agilent). That is the technology that will enable us to develop both the mid-bus probe and the slot interposer.

## Slide 58: PCI Express® 3.0 – Total Solution
Receiver Test
Transmitter Test
Interconnect Test
Protocol Test
(link/transaction layers)
SW
HW
Fixture
Signal Condi-tioning
N5990A Automatic SW for PCIe compliance
N5393C PCI Compliance Test Software
DSOX900000A Infiniium
real time
scope
U4301A
PCIe Analyzer
U4305A
PCIe Exerciser/
LTSSM
86100C
DCA-J
E5071C Option TDR ENA Network Analyzer
or
N4903B
J-BERT High-Performance Serial BERT
N4916B
De-emphasis
N4915A-014
Cal Channel
CBB2
CLB2
CBB2
CLB2
or
or
U4321A
PCIe Interposer Probe
CBB2
CLB2
or
U4322A PCIe mid-bus probe
PCI-SIG
Compliance boards
Motherboard
Rx
Tx
DUT
PCI-SIG
Compliance boards
PCI-SIG
Compliance boards
Tx
Transmitter
Rx
Receiver
Tx
Rx
Tx
Digital
Test
Console
...
Add-in Cards
Rx
Tx
∫∫
U4317A PCIe Adapter
Notes: Agilent, which has a 60% HDMI market share, has developed tools in the physical, data link and protocol layers to meet the challenges posed by the standard. The solutions are designed to reduce development costs, provide accurate test results and simplify the measurement processes for test engineers in the consumer electronics, cable manufacturer and semiconductor industries. Agilent's HDMI solutions are different than its competitors due to its full automation software testing capabilities, which speeds up testing; efficient electrical performance of the devices and fast test throughput, increasing productivity up to 50 percent. Furthermore, Agilent offers scalable solutions, considered an improvement in the HDMI market because companies now have the flexibility to test from 3-7 Gb per second.
Agilent’s source test solution is approved in all 7 test centers. Tek’s solution is only approved in 3 test centers.
The TMDS signal generator and cable emulator has lower noise than Tek.
Agilent offers a unique solution of integrated PAG with protocol test.

## Slide 59: PCIe 3.0 Products Protocol Trace Capture & Form Factor
M9502A
  2 slot AXIe Chassis
U4301A
    Protocol Analyzer module
  M9536A
      Embedded Controller
M9505A
  5 slot AXIe Chassis
  Shown with M9536A

## Slide 60: PCIe 3.0 Products Protocol Exerciser/Emulation
U4305A
  Root Complex/End Node emulator
U4305A-021
  Protocol Test Card 3.0 (PTC3)
  N5316A
      Backplane
      Supports 8.0, 5.0, & 2.5 GT/s

## Slide 61: PCIe 3.0 Products Protocol Trace Capture Probes
U4321A
Solid Slot Interposer Probe
U4322A
Full Width Midbus Probe (x8 bidirect)
U4324A
Flying Lead Probe (Solder Down)
U4317A
Gen2 to Gen3 Probe Adapter
N5426A
ZIF (zero insertion force) Tip Kit for U4324A

## Slide 62: Typical configuration for PCIe Gen3 analysis
Partnumber |  | Option | Description
Chassis |  |  | 
M9502A |  | M9502A | AXIe Chassis: 2-slot with Integrated System Module
 |  | M9502A-U20 | ESM with USB 2.0
M9536A |  | M9536A | AXIe Embedded Controller: Quad Core, 8GB RAM, 160 SSD, 2 GB/s
 |  | M9536A-M08 | Memory, 8GB Standard
 |  | M9536A-W76 | Windows 7 operating system: 64 bit
Gen3 Analyzer Module |  |  | 
 | U4301A-A08 |  | Analyzer linkwidth x8
Viewer upgrades |  |  | 
U4301A | U4301A-1FP |  | LTSSM Viewer, Fixed Perpetual License
 | U4301A-2FP |  | Performance Analysis Package, Fixed Perpetual License
 | U4301A-3FP |  | Transaction Decoder, Fixed Perpetual License
Gen3 Slot Interposer |  |  | 
 | U4321A-A08 |  | Slot interposer 3.0 for PCIe 8Gbps x8
Gen3 Flying Lead |  |  | 
U4324A | U4324A |  | Probe, Four Channel Flying Lead, ZIF Tip for PCIE up to 8Gbps
 | N5426A |  | ZIF Tip, Kit of 10

## Slide 63: Typical configuration for PCIe Gen3 analysis
Partnumber |  | Option | Description | Price (USD)
Chassis |  |  |  | 
M9502A |  | M9502A | AXIe Chassis: 2-slot with Integrated System Module | 8,087.00
 |  | M9502A-U20 | ESM with USB 2.0 | 550.00
M9536A |  | M9536A | AXIe Embedded Controller: Quad Core, 8GB RAM, 160 SSD, 2 GB/s | 9,323.00
 |  | M9536A-M08 | Memory, 8GB Standard | 0.00
 |  | M9536A-W76 | Windows 7 operating system: 64 bit | 0.00
Gen3 Analyzer Module |  |  |  | 
 | U4301A-A08 |  | Analyzer linkwidth x8 | 45,272.00
 | U4301A-AN3 |  | Analyzer software license for PCIe 8Gbps | 23,343.00
Viewer upgrades |  |  |  | 
U4301A | U4301A-1FP |  | LTSSM Viewer, Fixed Perpetual License | 1,545.00
 | U4301A-2FP |  | Performance Analysis Package, Fixed Perpetual License | 1,500.00
 | U4301A-3FP |  | Transaction Decoder, Fixed Perpetual License | 1,500.00
Gen3 Slot Interposer |  |  |  | 
 | U4321A-A08 |  | Slot interposer 3.0 for PCIe 8Gbps x8 | 18,377.00
Gen3 Flying Lead |  |  |  | 
U4324A | U4324A |  | Probe, Four Channel Flying Lead, ZIF Tip for PCIE up to 8Gbps | 8,813.00
 | N5426A |  | ZIF Tip, Kit of 10 | 563.00
 |  |  |  | 118,310.00

## Slide 64: Typical configuration for PCIe Gen2
Chassis |  |  | 
N5302A | N5302A | N2X 2-slot portable chassis | 5,632.00
Gen2 Analyzer Module |  |  | 
N5306A | N5306A | Analyzer Module for PCIe 5Gb/s (requires 2 for x 16) | 28,912.00
 | N5306A-A08 | Analyzer SW License x8 for PCIe 5Gb/s | 25,078.00
Interposer |  |  | 
 | N5315A-A08 | Slot Interposer x8 for PCIe 5Gb/s | 15,584.00
 |  |  | 75,206.00
Exerciser |  |  | 
N5309A | N5309A-E08 | Half Sized Exerciser and LTSSM Board x8 for PCIe 5Gb/s | 34,403.00
 | N5309A-EX2 | Exerciser SW License and LTSSM for PCIe 5Gb/s | 48,351.00
 | N5309A-PTC | Exerciser SW License PTC | 0.00
 | N5309A-COM | Exerciser SW License Compliance Assured Test Package | 17,759.00
N5316A | N5316A | Test Backplane for PCIe 5Gb/s | 6,953.00
 |  |  | 107,466.00
Jammer |  |  | 
 | N5323A-J08 | Jammer Module x8 for PCIe 5Gb/s | 33,220.00
 | N5323A-JM2 | Jammer SW License : Jammer at 5 Gb/s | 34,474.00
 | N5323A-SCR | Jammer SW License : Jammer Scripts | 8,635.00
 |  |  | 76,329.00

## Slide 65: Typical configuration for PCIe Gen3 exerciser
Partnumber | Option | Description | Quantity | Price (USD)
Exerciser Hardware; select lane width ( 1 Required) |  |  |  | 
U4305A | U4305A-E08 | Exerciser board x8 for PCIe 8Gbps | 1 | 57,744.00
License at least one required |  |  |  | 
 | U4305A-EX3 | Exerciser software license for PCIe 8Gbps | 1 | 37,377.00
 | U4305A-021 | Protocol Test Card (PTC) test suite | 1 | 5,253.00
Exerciser additional options - require EX3 option be purchased |  |  |  | 
 | U4305A-LT3 | LTSSM software license | 1 | 18,051.00
 | U4305A-1FP | NVMe test suite | 1 | 12,000.00
 | U4305A-021 | Protocol Test Card 3.0 software license | 1 | 5,253.00
 | U4305A-022 | Transaction layer end-to-end cyclic redundancy check (ECRC) software license | 1 | 3,152.00
PCIe Backplane |  |  |  | 
N5316A | N5316A | Test Backplane | 1 | 6,953.00
 |  |  | 1 | 145,783.00