## Slide 1
AGILENT RESTRICTED DO NOT INCLUDE SLIDE TO EXTERNAL AUDIENCES AGILENT RESTRICTED
AGILENT RESTRICTED DO NOT INCLUDE SLIDE TO EXTERNAL AUDIENCES
AE Training
Stateful TCP and Beyond

## Slide 2: Training Objectives
  At the end of this module you will be able to:
  Demonstrate basic TCP connection blasting
  Demonstrate TCP connection blasting combined with applied policy via diff-serv code-points and VLAN IDs
  Demonstrate triple play testing: stateful TCP testing with real application traffic in the presence of video and voice traffic
AGILENT RESTRICTED DO NOT INCLUDE SLIDE TO EXTERNAL AUDIENCES AGILENT RESTRICTED
AGILENT RESTRICTED DO NOT INCLUDE SLIDE TO EXTERNAL AUDIENCES

## Slide 3: Target Market
The Agilent N2X stateful TCP solution excels at in-lab test for the following scenarios:
Any kind of forwarding device: routers, switches (including enterprise devices)
Various access devices: BNGs (BRASs), BSRs, BSAs
Some security devices: IPS/IDS, and some portion of firewall functionality
√
√
√
N2X is designed to test the network infrastructure (but not servers or clients – that’s what NetworkTester is for) that delivers Triple Play services.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Differentiating Features
Bandwidth – scaling to GbE with a fully-featured TCP stack including re-transmissions, windowing and statefulness
Price!!: Equivalent SW-based solution from competitor (Ixia) is FIVE times as expensive!!
Integration: L2-7 on one port, stateful and stateless on one port
Usability: slider bar to control stateful traffic on-the-fly
Repeatability: run the same test 5 times, get the same result every time.
Bandwidth and price/bandwidth are the most important differentiators
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5
Feature #1: Line-rate stateful TCP
Achieve line-rate stateful TCP with a fully-featured stack, re-transmissions, and short packet lengths
Not possible with one port from a CPU-based solution
Competitors must gang together multiple ports to achieve GbE line rate
    VERY expensive: > US$300K, even at Cisco prices
    Clumsy to use a L2 aggregation device
    L2 device might have its own problems
  Slider-bar for stateful traffic control is very sexy
    Competitors must stop traffic each time to set new traffic load
    Slider-bar is a major ease-of-use competitive advantage.
Oh yeah!
Notes: Spirent can’t define per-subscriber channel zapping profiles.

## Slide 6
Integrated L2-7
L2-3 and L4-7 in same GUI, running on same port
In the same software application
Simultaneously
Feature #2: Integrated L2-7, VVD, stateful/stateless
Triple play (video, voice and data) traffic generation
Generate video using PDU builder (use currently hidden MPEG PDU)
Generate voice using PDU builder: RTP fill options
Integrated Stateful/ Stateless
Stateful connection groups and (traditional) stateless traffic running on same port
In the same software application
Simultaneously
Notes:   10-60 second clips that are ‘looped’ continuously
  Overriding theme at DSL forum meeting for scoping WT-126 Triple-play Service Quality of Experience (QoE) Requirements and Mechanisms
  was that video QoE cannot be considered in isolation. Video is always interacting with voice and data ..(and often gaming).
  Triple play service ‘bundles’ are critical reducing subscriber churn (69% of customers that have a service ‘bundle’ aren’t interested in changing service providers). Since bundles are the wave of the future, video traffic MUST be tested in the presence of other voice and data services.

## Slide 7
Feature #3: Fully-featured TCP Stack
  Show off N2X/Stateful TCP’s ability to customize the TCP stack according to the customer’s requirement
  Turn on/off various TCP mechanisms: Fast Re-transmit, Slow-start
  Set key parameters: MSS, IWS, MWS
  Shows parameters our competitors do not give access to
Notes: )

## Slide 8: Product Demonstration (Connection Blasting)
Load the pipe with stateful TCP traffic!
Characterize forwarding performance of stateful layer-4 traffic
Test at scale statefully and with re-transmissions!
Find the breaking point of your router with stateful TCP traffic!
bandwidth
time
N2X Port
Router
SUT
GbE
N2X Port
GbE
TCP state
TCP state
Control stateful TCP traffic load dynamically in real-time (on the fly)!!

## Slide 9: Product Demonstration (Triple-play Test)
Customers want to verify that their device or network is prioritizing traffic correctly according to policy, i.e. that the higher priority traffic such as IPTV and VoIP are not dropped in the presence of bandwidth-hogging peer-to-peer traffic
Customers ultimately want to perform QoE and QoS measurements on the IPTV and VoIP, and see clearly that bulk traffic such as P2P, FTP and HTTP is being dropped.
N2X Port 1
Router
SUT
GbE
N2X Port 2
GbE
TCP state
TCP state
N2X Port 3
N2X Port 4
P2P, HTTP, FTP
P2P, HTTP, FTP
IPTV Clients
VoIP Clients
IPTV Servers
VoIP Clients
Egress ports are oversubscribed causing congestion and packet dropping.

## Slide 10: Competitive Notes to Highlight
All competitors’ solutions use a software + CPU architecture. CPU-based solutions come in different flavors:
  Industrial PC platform (Spirent Avalanche)
  CPU on a dedicated test platform (L4-7 on Test Center, IxLoad)
Either way, these solutions suffer from the same limitations:
  Poor performance (cannot scale up in bandwidth)
  Poor usability (cannot adjust traffic on the fly)
  Inaccurate measurements
  No repeatability (get different results every time!)
  No integration on same physical port
  No integration in same SW application
  Expensive! Multiple times more expensive to reach same scalability

## Slide 11: Saved Test Measurements and Reports
VoIP + stateless TCP traffic
- 0 packet loss
- latency=350us
VoIP + stateful TCP traffic
  - packet loss 1 to 2%
  - (max) latency=2400us
switch (popular model)
N2X Port
N2X Port
1000Mb/s
100Mb/s
Input Traffic
VoIP Traffic: G.711/RTP/UDP @ 71Mb/s, DSCP=EF
Stateful background traffic: 32 TCP connections,
MSS=1640 bytes @ 3Mb/s, DSCP=default
Policing Applied in Switch
TCP policed to <25% (25Mb/s)
Output Traffic
96% of line rate (=71Mb/s + 25Mb/s)
Not over-subscribed
But packets are dropped! Delay added!
The only way to test the real impact of Data on IPTV and VoIP is to use Stateful Application traffic.

## Slide 12: Frequently Asked Questions
Please refer to:
https://partners.business.agilent.com/lit/lit_detail.asp?lid=7125

## Slide 13: Product Roadmap
  N2X Release 6.9 (July 2007)
  N5575A: Basic TCP connection blasting
  N5576A: Application simulation (HTTP, FTP, P2P) over TCP connections
  Under Investigation:
  N2X Release 6.10 (December 2007)
  Re-introduce capture (?)
  More simultaneous connections (at least 128K connections/port-pair)
  More application types for N5576A
  N2X in 2008
  10G stateful TCP
  Stateful TCP in integrated triple play solution
  Capture/Replay for N5576A
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Known Issues, Limitations and Workarounds
Capture is turned off for the stateful TCP personality. We re-used the normal N2X capture memory to hold TCP state. It might be possible to re-introduce capture in 6.10 – this point is being investigated. There are 3 workarounds for the lack of capture: DUT port-mirroring, using a TAP device, and using an unsupported QuickTest from Agilent/DNO
PPP & DHCP integration is only provided by the API in the first release.
Similar to PPP and DHCP, MAC addresses in the stateful TCP solution must be manually copied over from the normal N2X MAC address settings
QuickTests and scripts may be provided to do this with 6.9, and more complete integration will be added in 6.10

## Slide 15: Available Resources
Wikipedia:
    TCP: http://en.wikipedia.org/wiki/Transmission_Control_Protocol
IETF RFCs
    RFC 793: original TCP specification
    RFC 1122: Internet host requirements
    RFC 2581: explains TCP congestion control
    RFC 3168: explains ECN (Explicit Congestion Notification)
See also resources on next slide in launch plan

## Slide 16: Launch Overview
FAQ (Frequently Asked Questions): available now at:
https://partners.business.agilent.com/lit/lit_detail.asp?lid=7125
Technical Data Sheet: Complete: See external web site
White Paper: Complete! Ask Todd for copy
Sales Presentation: Complete: Ask Todd for copy
Beta Evaluations: Complete! (DT, Redback, Force10)
Press Release: Coming in June 2007 for NXTcomm in Chicago
Launch Tour:
Americas: Completed in March 2007
Europe: Completed in April/May 2007
Asia: Schedule for late May 2007

## Slide 17: Team Members
Product Manager: Todd Law
Project Manager: Stephen Caplan
Software Lead: Jenny Koo
Hardware Lead: Richard Hein
GUI Lead: Ryan Crawford
GUI Engineer: Fraser Loch
API Lead: Valentina Bozanovic
HW Engineer: Martin Mazur
Embedded Software Engineer: Li Zhao
Engineer: Sanja Denic
Engineer: Yuriy Olshevskyy
Support Lead: Luis Estrada
PQA Lead: Peggy Sah
Learning Product: Wendy Lee
Marcom Lead: Tara Van-Unen
AGILENT RESTRICTED DO NOT INCLUDE SLIDE TO EXTERNAL AUDIENCES AGILENT RESTRICTED
AGILENT RESTRICTED DO NOT INCLUDE SLIDE TO EXTERNAL AUDIENCES