## Slide 1: OpenLAB CDS Shared Services Level 1 Training AN-CE-NDS-1-149-x Module 1: OpenLAB CDS Introduction
Abel De Oliveira
Product Support Engineer
Software and Informatics Division / LPAD-LSG

## Slide 2: What is OpenLAB CDS?
OpenLAB CDS provides a common navigation layer while maintaining the instrument control interfaces that customers are used to using today.
3 major components comprise OpenLAB CDS:
      OpenLAB CDS Shared Services
      OpenLAB CDS EZChrom Edition
      OpenLAB CDS ChemStation Edition
      OpenLAB CDS serves as the new version of both EZChrom
      and multi-technique ChemStation:
      Supports latest LC and GC modules
      ChemStation supports single quad LC/MS
      QQQ, QTOF, and GC/MS stay on MassHunter and Mustang respectively.

## Slide 3: What is OpenLAB CDS?
Shared Services
Instrument Navigation Project Navigation
User management permissions
User Authentication
Software Diagnostics
Shared Components
Common Reporting
Common Drivers
Easy Sequence Wizard
  Bring in a shared services layer interface
  Keeping instrument interface/workflow the same
  Provide Scalability based on common installable components
EZChrom CDS Workflow
EZChrom Data Analysis
EZChrom Sequencing
EZChrom storage/ECM
Multi-Vendor Control
ChemStation CDS Workflow
ChemStation Data Analysis
ChemStation Sequencing
ChemStation storage/ECM/Data Store
Notes: 3

## Slide 4: Shared Services: Functions
Instrument Management
Create/edit instruments and instrument access
Central instrument status overview including activity logbook
Projects Management
Access security for data stored “in” projects
Manage application user privileges per project
Users / Groups / Roles Management
User authorization
Manage users and user groups
User privileges (roles)
Network Communication Infrastructure
Communication between different components of a C/S system
Diagnostics Infrastructure
Software diagnostics and tracing
Support for workstation as well as C/S systems
License Management
Application independent license management
Supports license server infrastructure
Customer portal for license management
Notes: Two main functions:
Administration: creation and configuration of instruments, management of group / projects / users
Multi-instrument view: Centrally manage access to instrument and view the instrument status.

## Slide 5: OpenLAB CDS Scalability
Workstations
Networked Workstations
Distributed CDS-File based (EZChrom Only)
Enterprise OpenLAB CDS with ECM Enterprise
Increasing Users/Instruments
Distributed OpenLAB CDS with ECM / Data Store Workgroup
Increasing Functionality
Notes: Same look and feel independent of scalability
Supports scaling (lab at a glance)

## Slide 6: Supported Topologies Standalone Workstation
EZChrom or ChemStation
Up to 4 instruments per workstation
Administration and instrument management
Two or more standalone workstations can be on the same network, but they need to be managed independently.
Notes: EZChrom and ChemStation can be installed as workstations. The application and the OpenLAB CDS Shared Services are installed on the same computer. Up to 4 instruments can be configured on the workstation.

## Slide 7: Supported Topologies Networked Workstation
EZChrom or ChemStation
Central administration, license and instrument management
Up to 4 instruments per networked workstation
Central status overview for all instruments
ChemStation – local disk storage only.
EZChrom – central file storage only
OpenLAB Server must reside on a dedicated server and not an instrument workstation
EZChrom
only
File
Server
Notes: EZChrom and ChemStation can be installed in Networked workstation. Up to 4 instruments can be configured on the workstation. The OpenLAB Shared Services server must reside on a dedicated server and not an instrument workstation .
Data storage is a local one for ChemStation and a central one for EZChrom.
Advantage over Standalone: License and user administration is done in one central place.

## Slide 8: Supported Topologies Distributed CDS (Simple)
Central Administration and Instrument management
Remote access of instruments & data processing via network using CDS Clients
EZChrom Edition :
  Up to 4 instruments per instrument controller (AIC)
  Central file storage
ChemStation Edition:
  Up to 10 instruments per instrument controller (AIC)
  ECM is mandatory
Notes: Instruments and data processing are accessed remotely via the network from Client computers.
Every client can access every instrument.

## Slide 9: Supported Topologies Distributed CDS (Complex)
Following components may be hosted on independent machines
Shared Services
Licensing
Database
Storage Path for EZChrom (Enterprise path/Project root)
Notes: This topology is available for EZChrom only. Up to 4 instruments can be defined per instrument controller. Instruments and data processing are accessed remotely via the network from Client computers.

## Slide 10: Supported Topologies Standalone Compliant Workstation
ChemStation only, introduced with revision C.01.06.
Up to 4 instruments per workstation
Administration and instrument management locally
Local backend (Data Store) for CFR Part11 compliance.
Notes: This is the equivalent of the ChemStation Plus solution (ChemStation + ChemStore standalone + Security Pack).

## Slide 11: Summary
  New common navigation interface (OpenLAB Control Panel)
  Provides nearly identical front end workflows for both ChemStation and EZChrom Editions.
  A Variety of configurations are available from a common installer model in order to support customer needs with a minimum set of software components.
  System Scalability
 Next Up: OpenLAB CDS Installation