## Slide 1: 1100/1200 Instrument LAN IP Address Management
G4208A Instant Pilot (IP) Setup Screen
Allows modifications of the LAN/LAN card settings.
Notes: This is the view from the welcome screen

## Slide 2: 1100/1200 Instrument LAN IP Address Management
G4208A Instant Pilot (IP) Setup Wizard
For parameters, refer to the installed LAN
card’s documentation
Allows modifications of the LAN/LAN card settings.

## Slide 3: 1100/1200 Instrument LAN IP Address Management
G4208A Instant Pilot (IP) Setup Wizard
Allows modifications of the LAN/LAN card settings.
Allows changes to the LAN card settings
When finished press Done to write the new values.

## Slide 4: 1100/1200 Instrument LAN IP Address Management
G4208A Instant Pilot (IP)-configure screen
Allows modifications of the LAN/LAN card settings.
Allows changes to the LAN card settings
.

## Slide 5: 1100/1200 Instrument LAN IP Address Management
G4208A Instant Pilot (IP)-configuration screen
Allows modifications of the LAN/LAN card settings.
Allows changes to the LAN card settings
When finished press Done to write the new values.

## Slide 6: 1100/1200 Instrument LAN IP Address Management
G4208A Instant Pilot (IP)-configuration screen
Allows modifications of the LAN/LAN card settings.
Allows changes to the LAN card settings
When finished press Done to write the new values.

## Slide 7
Appendix- Establishing communication with a Hand Held Controller
Using a Telnet Session to disable BootP
Using Internet Explorer to disable BootP

## Slide 8: 1100/1200 Instrument LAN IP Address Management
Setting the IP address and Subnet Mask by using the BootP Server and disabling the BootP request with a Telnet Session
Normally if you power cycle the module which contains the JetDirect Card, a BootP request shall be send out by the card. The BootP server will respond to the instrument IP requests and supply the instrument JetDirect card with an IP address, a subnet mask and other necessary transfer parameters.
With the help of the BootP Server, you can set a fixed IP address and subnet mask. With a Telnet session we can disable the further BootP requests.

## Slide 9: 1100/1200 Instrument LAN IP Address Management
1. Assign an IP address and Subnet Mask with the BootP server/service.
2. Open a Telnet Session by typing “telnet” followed by the IP address you was assigning to the JetDirect Card
Telnet Session

## Slide 10: 1100/1200 Instrument LAN IP Address Management
That will open a Telnet session as shown
Telnet Session

## Slide 11: 1100/1200 Instrument LAN IP Address Management
Type “/” on the prompt line to read out the JetDirect Card
NOTE: in Windows XP you will not see “/” when you type it
Telnet Session
Notes: There is no echoing turned on…

## Slide 12: 1100/1200 Instrument LAN IP Address Management
Notice the “Config By” listing…
In this case it is by BootP…
Telnet Session

## Slide 13: 1100/1200 Instrument LAN IP Address Management
To Disable the BootP request you have to type the IP address on the prompt line…
IP:192.168.254.11
…then press enter
NOTE: in Windows XP you will not see what you are typing
Caution! Be sure of what you are entering
Telnet Session

## Slide 14: 1100/1200 Instrument LAN IP Address Management
Notice the “Config By” now states “User Specified”
Telnet Session

## Slide 15: 1100/1200 Instrument LAN IP Address Management
As long as you know the IP Address of the JetDirect card then you can use Telnet to ‘reset’ the card to defaults…
Open a telnet session
Type in / and press Enter to list current settings
Type in cold-reset and press Enter to reset the card
It should respond with…
Type in quit and press Enter to complete the card reset
Internet Explorer

## Slide 16: 1100/1200 Instrument LAN IP Address Management
If you know the IP Address then there is another way to look at things…using Internet Explorer (IE)
Type in the IP Address of the JetDirect card and click Go
Internet Explorer

## Slide 17
This does not work in all cases, but when it does you will see this Jet Admin Software Home Page from the card itself.
Notice: the FW Ver. Number (32-bit requires K.08.32 or higher)
Internet Explorer

## Slide 18: 1100/1200 Instrument LAN IP Address Management
Click on the Administration button and wait
Internet Explorer

## Slide 19: 1100/1200 Instrument LAN IP Address Management
Click on the Configuration tab.
Under TCP/IP: Protocol
Notice: the setting for “TCP Config Type” here it is set to BootP
Internet Explorer
Notes: the setting for “TCP Config Type” here it is set to BootP meaning that at every power on it will send out a BootP request

## Slide 20: 1100/1200 Instrument LAN IP Address Management
Click on the Configuration tab.
Notice: section titled Enable Protocol Stacks All 4 protocols must be checked!
Under TCP/IP: Protocol
Notice: the setting for “TCP Config Type” here it is set to BootP however it can be set to ‘manual’ or ‘DHCP’
Internet Explorer
Notes: Notice: the setting for “TCP Config Type” here it is set to BootP however it can be set to ‘manual’ or ‘DHCP’
Manual meaning that it already has a ‘fixed’ IO Address and it will not send out a BootP request at power on.
DHCP (Dynamic Host Configuration Protocol) technically we do not support this, but if the customer insists upon it there is a white paper on how to set it up at their own risk.
The 4 protocols in the Enable Protocol Stacks must be checked, if they are not then when you boot up the PC and open the ChemStation the first time it will work fine, however if you close the ChemStation and then try to open it again it will not open. Rebooting the PC will again let it open the first time but not the second time.

## Slide 21: Setting Communication using Handheld Modules
Control Module (Da Vinci)
Instant Pilot (Hobbit)
Notes: Manual configuration only alters the set of parameters stored in the non-volatile memory of the card.
It never affects the currently active parameters. Therefore, manual configuration can be done at any time.
A power cycle is mandatory to make the stored parameters become the active parameters, given that the initialization mode selection switches allow it.

## Slide 22: Manual Configuration
Notes: Manual configuration only alters the set of parameters stored in the non-volatile memory of the card.
It never affects the currently active parameters. Therefore, manual configuration can be done at any time.
A power cycle is mandatory to make the stored parameters become the active parameters, given that the initialization mode selection switches are allowing it.

## Slide 23: 1100/1200 Instrument LAN IP Address Management
Setting the IP address and Subnet Mask and disabling the BootP request by using the handheld controller.
Normally if you power cycle the module which contains the JetDirect Card, a BootP request shall be send out by the card. The BootP server will respond to the instrument IP requests and supply the instrument JetDirect card with an IP address, a subnet mask and other necessary transfer parameters.
With the help of the handheld controller (G1323A/B), you can set a fixed IP address, subnet mask and disable the BootP request.

## Slide 24: 1100/1200 Instrument LAN IP Address Management
G1323B Hand-Held Controller

## Slide 25: 1100/1200 Instrument LAN IP Address Management
G1323B Hand-Held Controller

## Slide 26: 1100/1200 Instrument LAN IP Address Management
G1323B Hand-Held Controller

## Slide 27: 1100/1200 Instrument LAN IP Address Management
G1323B Hand-Held Controller

## Slide 28: 1100/1200 Instrument LAN IP Address Management
G1323B Hand-Held Controller

## Slide 29: 1100/1200 Instrument LAN IP Address Management
G1323B Hand-Held Controller

## Slide 30: 1100/1200 Instrument LAN IP Address Management
G1323B Hand-Held Controller

## Slide 31: 1100/1200 Instrument LAN IP Address Management
G1323B Hand-Held Controller

## Slide 32: 1100/1200 Instrument LAN IP Address Management
G1323B Hand-Held Controller

## Slide 33: 1100/1200 Instrument LAN IP Address Management
G1323B Hand-Held Controller

## Slide 34: 1100/1200 Instrument LAN IP Address Management
G1323B Hand-Held Controller

## Slide 35: 1100/1200 Instrument LAN IP Address Management
G1323B Hand-Held Controller

## Slide 36: 1100/1200 Instrument LAN IP Address Management
G1323B Hand-Held Controller