## Slide 1: INTRODUCING GEM: General-Purpose Electronic Measurement Division and the Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs
Jim Durr
Application Support Engineer
David Tu
Application Engineer
Public Introduction
June 17, 2013
34460A / 34461A
Slides and documents (√) available at: ftp://ftp.agilent.com/mpusup/3446xA/TCC_Training

## Slide 2: GEM Marketing Organization

## Slide 3: Application & Support Organization
Lim, Hock Eng | Apps Focus : RF & Audio Product Contact : Power Meters
Lee, Chin Aik | Apps Focus : RF & Audio Product Contact : Audio Analyzer
Tan, See Kai | Apps Focus : Green Energy & Manufacturing Product Contact : Bench Instruments
Tu, David | Apps Focus : Green Energy & Manufacturing Product Contact : Bench Instruments
Wong, Sook Wai | Apps Focus : Maintenance & Installation Product Contact : Handhelds
Diller, Cheryl | Operations, Loveland
Chua, Teong Keat | Operations, Penang
Choi, Mun Ken | PMPS & Audio (Asia + Japan)
Durr, Jim | Counters, DMM, Pxi
Hornburg, Luke | FG, DMM
Lim, Say Heng | VEE, IO
Loh, Keh Teong | MI, Thermal, Hybrid, PLRO,PLPW
Wong, Seok Jin | HH, 5.5d DMM
Conway, Tom (NAW) | DAQ, DSA, DMM
Rose, Matthews (NAW) | PMPS & Audio (Americas + Europe)
Application Support Team
Fong Hong Kee
Application Team
Objective : Product Preference
Generation.
Technical Collaterals
Target Market Engagement
Training, Trade Show & e-Marketing
Support Team Yapp Poey Hee
Objective : Product Works as advertised
Service Levels
Warranty Cost
Training, e-Marketing

## Slide 4: GEM Product Portfolio
We are #1 player in Power Meter/Sensor, Counter, DMM, & Function Generator

## Slide 5: GEM Order Profile By Region
Chart: 
| Americas | EMEA | Japan | G. China | KSAP
GEM | 59.944 | 38.447 | 20.504 | 37.567 | 15.451

## Slide 6
The 34401A 6½ Digit DMM
From customers:
“trusted”, “very reliable”, ”perfect product”,
“the workhorse”
Introduced in 1991
Highest volume selling product in EMG history
~400,000 units world-wide!!

## Slide 7
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs
Full 34401A SCPI compatibility (34461A is the direct replacement)
Designed by the same team of engineers as the 34401A
System Identify: Shift → Utility → System Setup → User Settings → SCPI ID SYSTem:IDENtify HP34401A
Notes: 7

## Slide 8
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs Full 34401A SCPI Compatibility
No compatibilty mode to enable - accepts 34401A commands directly
Programming and compatibilty differences document (√)
No 34401A Discontinuance date announced > anticipated: 7/2014 – 7/2015
http://cp.literature.agilent.com/litweb/pdf/5991-2367EN.pdf
√

## Slide 9
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - A look at the products
34460A
34461A
Notes: 9

## Slide 10
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - side by side comparisons
Physical Dimensions (rack dimensions):
34460A/34461A: 272.3 mm (D) x 212.8 mm (W) x 88.3 mm (H) 34401A: 348.3 mm (D) x 212.6 mm (W) x 88.5 mm (H)
* Kit - no installation
* Customer Installable
* Software License
* Software License

## Slide 11
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - With no RS-232 interface, how is the 34461A a direct replacement?
RS-232 (PC) to LAN (Instrument) Converter identified
Proof of concept complete
Compatible with Agilent IO Libraries
Utilizes a LAN-Socket connection
Availability and configuration information posted on ‘GPETE’ blog http://gpete-neil.blogspot.com/
Not an Agilent supported interface configuration

## Slide 12: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Service and Support
3-year warranty (standard)
Whole Unit Exchange > Front panel/processor board > Fuses, battery, fan, bumpers > power module, transformer
1-year calibration Interval > adjust always (electronic adjustment) > standard and Z540.3

## Slide 13: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Service and Support
Can use existing 34401A Calibration Equipment
34460A/34461A
34401A

## Slide 14
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
USB File Transfer (drag/drop driverless connectivity)
Media Transfer Protocol (MTP) > Read only
> Data files (.csv)
> Instruments states (.sta)
> Images (bmp, png)
> Operating and Service Guide (pdf – 1.09 release)
USB Interface
Agilent IO Libraries (free)
Easy File Access
Access via Windows Explorer
USB
Windows Explorer View

## Slide 15
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
USB File Transfer (drag/drop driverless connectivity)
Modes of Operation: Shift → Utility → I/O Config → USB Settings
- USB: USB programming only
34461A – file access on (1C07), file access off (1A07)
34460A – file access on ( 1D07), file access off (1B07)
Easy File Access
- Composite: drag/drop and USB programming
- MTP: Drag/drop only, no USB programming or IO Library access
Composite and USB modes change the USB address – alias is not changed

## Slide 16
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
USB File Transfer (drag/drop driverless connectivity)
Shift → Utility → I/O Config → USB Settings → File Access (On)
Shift → Utility → I/O Config → USB Settings → File Access (Off)
Windows XP: Requires Microsoft Windows Media Player 11 for XP
Restricted function: instrument security must be unlocked
Power cycle required to enable/disable setting
Not supported on Mac/Safari
Easy File Access

## Slide 17
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
USB File Transfer (drag/drop driverless connectivity)
Example
Acquire → Trg Src (Single) → Samples/Trigger → Single → Save Readings (Internal)
Open Explorer and scroll to Agilent DMM
Easy File Access

## Slide 18
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
Instrument Security / NISPOM Sanitization (product Option SEC)
Shift → Utility → Test/Admin → Security → Secure Code (unlock)
Factory setting: AT3446XA
Security code override – procedure in operating/service guide
Security document location: (√) www.agilent.com/find/security

## Slide 19
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
Probe Hold
Shift → Probe Hold → Probe Hold (On)
Audible ‘beep’ when reading is obtained
Last 8 measured values listed (readings scroll)
Allows focus on test points rather than DMM display

## Slide 20
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
Graphical Displays
Number
Bar Meter
Trend Chart
Histogram
Display → Display

## Slide 21
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
Selectable back ground colors
Shift → Utility → System Setup → User Settings → Display Options → Colors

## Slide 22
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
Limits and Statistics
Shift → Math → Limits → Limits Shift → Math → Statistics → Statistics
Graphical representation of mean and 1-σ standard deviation; cumulative frequency distribution

## Slide 23
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
Save readings within any display mode
Acquire → Trg Src (Single) → Samples / Trigger → Single → Save Readings

## Slide 24
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
10A Current Range
6 ½ Digit Resolution
34461A only
Front panel terminals only
Current path fuse located internally

## Slide 25
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
10A Current Range
Reduce burden voltage through less shunt resistance
34461A 3A current shunt resistance
34461A 10A current shunt resistance

## Slide 26
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
Temperature Measurements
Temp → Probe
Thermistor: 5k (2W/4W)
RTD: PT100 (2W/4W)

## Slide 27
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
Help System
Press and hold any key (hard or soft) for context-sensitive help
Shift → Utility → System Setup → User Settings → Help Lang
Help languages: English, French, German, Japanese, Korean,
Chinese, Russian

## Slide 28
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
“Mobile Optimized” Documentation (eDoc)
Shift → Help → Select
1. Scan the QR code directly from the instrument front panel to view
the operating and service guide.
→

## Slide 29
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
Web UI

## Slide 30
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
Web UI – release 1.09
Will eventually replace the Product
Reference CD

## Slide 31
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
Web UI – Monitor DMM/Control DMM

## Slide 32
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
Web UI – DMM Overview / Current SCPI Configuration
*LRN? String

## Slide 33
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
Firmware Update Utility
New Utility Allows update using LAN, GPIB, or USB Interface

## Slide 34
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
Firmware Update Utility
Front Panel USB Host Port
> automatic USB drive configuration
Press ‘Update… to create required directory and files on USB root

## Slide 35
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
On-Line Examples
http://www.agilent.com/find/34461A
Visit Technical Support → Drivers, Firmware, & Software

## Slide 36
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Product Features
Videos
Digital Multimeter Programming in Visual Studio
https://www.youtube.com/watch?v=GwZ2Kv9L-Xg
Digital Multimeter MATLAB Programing Example
https://www.youtube.com/watch?v=lVpMH4NDOpE

## Slide 37: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
www.agilent.com/find/DMMUtilitysoftware

## Slide 38: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
System Requirements
PC Operating Systems (Supported)
- Windows 8, 32-bit and 64-bit (Windows 8, Windows 8 Pro)
- Windows 7, SP1 32-bit and 64-bit (Professional, Enterprise, Ultimate)
- Windows XP, SP3 32-bit (Professional)
PC Hardware
- Windows 8 and Windows 7:
Processor: 1 GHz or faster (2 GHz or greater recommended)
RAM: 1 GB (32-bit) or 2 GB (64-bit) (3 GB or greater recommended)
Windows XP:
Processor: 600 MHz or faster (1 GHz or greater recommended)
RAM: 512 MB (1 GB or greater recommended)
Web connection required for installation and upgrades

## Slide 39: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Supported Instruments
Agilent 34401A, 34405A, 34410A, 34411A, 34450A, 34460A, and 34461A DMMs.
Note:
- Digitizing is supported only on 34410A, 34411A, 34460A, and 34461A DMMs
- Does not work with 3458A, 34420A, L4411A or any PXI DMM
- Does not support any Handheld DMMs or U3400 series
- Up to 9 DMMs per connectivity session (tested)
Supported Interfaces
USB, GPIB, LAN, RS-232.
Requires Agilent IO Libraries Suite v16.0 or later
Works with NI Max

## Slide 40: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Installation
104MB download – no CD, web distribution only
Automatically installs required dependencies
Included in the install package
- .NET 4.0
- MATLAB binary (for export)
- Agilent connectivity fabric
IO Libraries are automatically downloaded and installed if required

## Slide 41: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Basic Operation
Starts by reading DMM state, app does not have pre-defined state
Direct control of SCPI functions
Available functions reflect features of connected DMM
Actions take effect immediately (commands are sent to instrument as functions are changed)

## Slide 42: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility

## Slide 43: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Basic Operation – The Bench
Start an App (App states)
Play All/Stop All
Panel Views
Simulation Mode

## Slide 44: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Basic Operation – Pop in/out
Access to instrument control

## Slide 45: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Basic Operation – Pop in/out

## Slide 46: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Basic Operation – Histogram and Table Views

## Slide 47: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Chart Features
Zooming/Panning
Markers
Measurements
Axis Labels
Auto Scroll
Scale and Autoscale Y

## Slide 48: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Datalogger/Digitizer
Datalogging – PC Paced
- Measurement rate
  can be paced by DMM settings
  PC paced measurements have 20ms min (approx.)
- Flexible start/stop control
- Alarms with notification

## Slide 49: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Datalogger/Digitizer
Digitizer – DMM paced
Pre-trigger samples not supported

## Slide 50: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Exporting Data Files
Export
- Exports all data
- Select range to limit size
- Bench level export is different than app
- MATLAB not required for export to MATLAB files
Data File Compatibility
- Can open Intuilink DMM setup files
- Exports to CSV, MATLAB, Excel, Work
- Bitmaps saved as BMP, JPG, PNG
- Data logs saved in proprietary format, use data manger to export

## Slide 51: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Exporting Data Files
Data log files stored in a fixed directory location
Files cannot be viewed directly
No limit on file size or data log period
Performance decrease above 100k points

## Slide 52: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Example (digitizing)
Input: 1 Hz, 2 Vpp sine wave
Set up Mode: Digitizer Measurement: DC voltage Range: 1V NPLC: 0.02 Impedance: 10M Auto Zero: Off Mode: Digitizer Trigger Source: Immediate Sample count: 10k Trigger Delay: 92 uSec

## Slide 53: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Example (digitizing)
At a 1 Hz rate and a sample count of 10k readings, 10 cycles in the graph represent 1000 readings/second. Setting a trigger delay of 92 us produces almost exactly 1000 readings/second. Setting a delay of 0s results in the readings being acquired over approximately 9 cycles (> 1000 readings/second).

## Slide 54: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Example (digitizing - exporting)
Exports from “main” tile

## Slide 55: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Additional Features
SCPI Log / Instrument Reset
- from “pop out” window

## Slide 56: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Additional Features
Application Help
- from “pop out” window - additional help topics
- from “main” tile

## Slide 57: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Issues
If PC enters ‘sleep mode’ while data logging the utility must be restarted
.NET install time: on some XP systems installation of .NET may take 45 minutes or hours to complete. Not common, but it has occurred and will eventually complete.
Initial startup may result in a error if after started too soon after installation
DMM can lockup if timeouts occur. Use device clear or reset the DMM

## Slide 58: Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - Digital Multimeter Connectivity Utility
Mobile Application
Mobile Devices
Apple iPhone, iPad, iPod Touch all models; iOS 5.0 and later
Connects directly to LAN DMMs (no LAN-GPIB converters)
Only works while the app is active
Does not data log or digitize while it is in background
Be aware of iPad memory limitations
Delete the application to clear the data files
www.agilent.com/find/DMMUtilitysoftware

## Slide 59: Q&A

## Slide 60
Agilent Truevolt 34460A / 34461A 6 ½ Digit DMMs - A look at the products
Notes: 60